## Slide 1: Future background scenarios in LCA
Romain Sacchi | October 15th 2024
Laboratory for Energy Systems Analysis
Paul Scherrer Institute, Switzerland
Grosshöchstetten, 12 November 2024
Center for Nuclear Engineering and Sciences
Center for Energy and Environmental Sciences

## Slide 2: Talk content
Definition of scenarios
Foreground vs. background scenarios
Integrated Assessment Models
PREMISE workflow and open-source tools
Effects of temporally-adjust inventories
Study cases using temporally-adjusted background LCA
Upcoming developments
System-wide prospective LCA
Notes: I would like to focus in this talk on background scenarios.
Background prospective scenarios are different from foreground prospective scenarios.
For some foreground systems, the background does not matter much.
But others are very much influenced by what is happening in the rest of the economy.

## Slide 3: What is a scenario?
A scenario is a description of how the future may develop, based on a coherent and internally consistent set of assumptions…
about key drivers including demography, economic processes, technological innovation, governance, lifestyles, and relationships among these driving forces (IPCC 2021)

## Slide 4: Different kinds of scenarios
Broad (global) scenarios
For the global economy (CGE models, IAM)
  Relevant for prospective LCAs in general
    Background scenarios
Narrow (local) scenarios
For specific technologies (hydrogen)
  Limited to a specific prospective LCA
    Foreground scenarios
vs
Yujing Guo et al 2019

## Slide 5
LCA is about systematically accounting for environmental impacts associated with a service, considering supply chain relations between processes.
pLCA is about projecting changes in process efficiency and supply chain relations, both in foreground and background, following on a coherent storyline.
Foreground
Background (LCA database)
Notes: 0. We typically distinguish the foreground from the background data structure in life-cycle modelling
Foreground modelling: comprises the process the system under study directly affects or is supported by.
Background modelling: ancillary services and commodities (metals, electricity heat).

## Slide 6
Current
2030
2050 2100
Current
Page 6
October 2nd, 2024
INTEGRATED ASSESSMENT MODELS (IAM) vs. LCA

## Slide 7: Foreground and background scenarios
Foreground system
Background system
EV use
EV production
Electricity mix
Foreground scenarios:
How will the EV of 2030 look like? How will it be used?
Background scenarios:
How will supply chains in the wider economic system of 2030 look like?
Important, but difficult to consider (at least by individual stakeholders)
A car manufacturer wants to make an LCA for an EV (electric vehicle) in 2030:
Fossils
Renewables
Steel
Batteries
Notes: The foreground system is under the influence of the manufacturer.
The background system is outside the sphere of influence of the manufacturer.

## Slide 8: Temporal consistency
A car manufacturer wants to make an LCA for an EV (electric vehicle) in 2030:
2030
2020
2030
2030

Foreground system
Background system
EV use
EV production
Electricity mix
Fossils
Renewables
Steel
Batteries
Notes: Combining foreground and background scenarios also allows for ensuring temporal consistency: the electricity mix (determined by the background scenario) aligns with the foreground scenario along the time axis.

## Slide 9: Narrative consistency
Foreground system
A car manufacturer wants to make an LCA for an EV (electric vehicle) in 2030:
optimistic
pessimistic

optimistic
optimistic
EV use
EV production
Electricity mix
Fossils
Renewables
Steel
Batteries
?
Background system
Notes: Combining foreground and background scenarios allows to see the impact of the factors outside of the manufacturer’s influence on the results.
In the case of an EV, the development of the electricity system is crucial and determines impacts.

## Slide 10: Our economy is deeply interlinked!
E.g., electricity mix affects:
  EV use
  EV production
  Materials/components production
But greener raw materials also improve the electricity mix and most other products!
  Feedback loops
 Broad future (background) scenarios help LCA practitioners to consider the combined effect of future changes
Foreground system
Background system
EV use
EV production
Electricity mix
Fossils
Renewables
Steel
Batteries
Vehicle energy use
Easy
Power plant share
Difficult
to model for an LCA practitioner
Power plant efficiency
Difficult
Notes: Indirect effects:
- Solar PV will be even greener if produced with green electricity and raw materials
- Wind power will become greener if steel decarbonizes thanks for secondary steel production, which itself uses greener electricity.

## Slide 11: Terminology “pLCI database”
pLCI database = prospective life cycle inventory database
    The difference with a regular LCI database is that it represents the economy, industrial activities, and trade for a future point in time under a given scenario.
Current
2030
2050 2100

## Slide 12: A short and incomplete history of pLCI databases
NEEDS project (2004-2009)
  First systematic approach to generate future scenarios of the ecoinvent database (electricity supply and other sectors)
THEMIS model (Gibon 2015; Hertwich 2015)
  Hybrid (MRIO-LCA) model including IEA energy and NEEDS scenarios
“When background matters” (Mendoza and Cox 2018)
  Combine data from the integrated assessment model IMAGE and ecoinvent (focus electricity supply)
  IAMs model SSPs (Shared Socio-economic Pathways) and RCPs (representative concentration pathways)
wurst: python package for systematic modifications of LCI databases (Mutel, 2017)
premise (Sacchi 2022)
  python package for generating pLCI databases
  Strongly based on IAM data (IMAGE, REMIND)
  Electricity, steel, cement, transport, fuel
Notes: SSP = global story lines
RCP = GHG concentration trajectories adopted by the IPCC describing different climate futures
The modeling of future background scenarios goes back at least to the NEEDS project, which has developed future scenarios for the European electricity supply more than 10 years ago. Later the THEMIS model was developed, which combined LCA with MRIO data and included scenarios of future electricity supply and other sectors. Then in 2018, Mendoza and colleagues coupled the Integrated Assessment Model IMAGE to the ecoinvent database to derive future versions of ecoinvent with a focus on electricity supply. This work is very interesting for two reasons: 1) it combines data from IAMs with LCA. IAMs model global future scenarios with detailed technology descriptions for important sectors. IAMs also implement the widely accepted Shared Socioeconomic Pathway scenarios. Thus using IAM data to generate scenarios for LCA takes some of the burden of generating scenarios from the LCA community. 2) the models were combined in a programmatic way using dedicated python libraries. This has several advantages, e.g. concerning reproducibility and transparency, but also the possibility to further extend and improve these libraries in future work. Lately, Sacchi and colleagues have extended this work in the PREMISE framework and further increased the sectoral coverage.

## Slide 13
REMIND
IMAGE
GCAM
MESSAGEix
TIAM-UCL
Integrated Assessment Models (IAMs) assess the interactions between human and natural systems
Contain stylized representations of
  Energy system
  Agricultural economy
  Climate
  Land system
Bridge the Science/Policy interface
  Scenario Analysis: What if?
  What are the drivers or constraints of change?
  How do technology and policy choices lead to different outcomes?
  Uncertainties? Sensitivities?
INTEGRATED ASSESSMENT MODELS (IAM)

## Slide 14
Global regionalized models that consider broad socio-economic and technological developments and their consequences over time.
Used to inform policymakers on climate change and other environmental or socio-economic criteria.
IPCC 2021
Paris agreement (~1.5 °C warming by 2100)
No additional climate policy
(~5 °C warming by 2100)
Shared-Socioeconomic Pathways (SSPs)
Representative Concentration Pathways (RCPs)
INTEGRATED ASSESSMENT MODELS (IAM)

## Slide 15: Socio-economic and climate constraints
Food demand
Population
Global Mean Surface Temp. Increase
Socio-economic constraints (SSP)
Climate constraints (RCP)
Credit: CarbonBrief, Zeke Hausfather, 2018. https://www.carbonbrief.org/explainer-how-shared-socioeconomic-pathways-explore-future-climate-change
CO2-eq emissions

## Slide 16: Projections on energy-intensive sectors
For each time step:
Technology investments
Capacity build-up
Generation
Link to dashboard

## Slide 17: Premise workflow
Steps
1) Input data: future scenarios from IAMs and the LCI database ecoinvent
2) Integration of future scenario data with the LCI database via premise
3) Export of pLCI databases in various formats
4 & 5) optional feedback of environmental indicators to IAMs
REMIND
IMAGE
MESSAGEix
Superstructure
1
2
3
4
5
No climate policy
Paris Agreement target
Nationally-determined contributions
Push for biofuels
Additional inventories to represent emerging technologies
Wurst
Constructive geometries

## Slide 18: Premise workflow: Open-source python packages
Brightway: LCA framework
Wurst: systematic transformations of LCI datasets
Constructive geometries: handling of ecoinvent geographies
Premise: integration software for IAM (and other) data with LCI databases
Superstructure approach: conversion of multiple LCI databases into a single LCI database (superstructure) and a scenario difference file [based on Brightway]
Activity Browser: graphical user interface to Brightway; implements “scenario-LCA” based on superstructure approach [based on brightway]
REMIND
IMAGE
MESSAGEix
Superstructure
1
2
3
4
5
No climate policy
Paris Agreement target
Nationally-determined contributions
Push for biofuels
Additional inventories to represent emerging technologies
Wurst
Constructive geometries

## Slide 19: OVERVIEW of open-source tools in the BRIGHTWAY ecosystem

## Slide 20: What does premise do?
Power
Create regional electricity markets
Adjust power plant efficiency
Fuels
Create regional fuel markets Add new production pathways (synthetic fuels)
Metals recycling
Adjust critical raw materials use
Adjust future recycled content
Hot pollutant emissions
Adjust hot pollutant emission
from GAINS
Transport
Create market for passenger
and freight road transport
Industry
Adjust efficiency for cement and steel production (fuel mix, process efficiency, material composition, etc.)
Carbon capture and storage
Add carbon capture and
storage where needed
Renewables
Adjust solar PV and wind turbines efficiency
80%
ongoing

## Slide 21: Example of SECTOR-SPECIFIC transformation: power generation
Efficiency
20%
40%
2020
2050
1 kWh
Hard coal
Lignite
Natural gas
Fuel oil
…
Pollutants
2 mg
4 mg
2020
2050
1 kWh
SOx , NOx, VOC, …
Market mixes
2050
USA
Relinking
Market
USA
Steel
USA
Farming
USA
IAM
LCA
LCA
Modelling new power plants
Scores relative to original Ecoinvent values

## Slide 22: Example of SECTOR-SPECIFIC transformation: TRANSPORT
Modelling new vehicles
Adjust fuel mixes
Market mixes
Relinking
Steel
USA
Farming
USA
Market
USA
IAM
LCA
LCA
Efficiency
20%
40%
2020
2050
CO2
Scores relative to original Ecoinvent values

## Slide 23: Example of SECTOR-SPECIFIC transformation: CEMENT
Modelling new kiln technologies
Adjust fuel mixes
CO2
Market mixes
Relinking
Concrete
EUR
Mortar
EUR
Market
EUR
IAM
LCA
LCA
Specific energy use
3.0
4.5
2020
2050
Efficient kiln
CCS (MEA)
CCS (Oxyfuel)
CCS (Direct Separation)
CCS (MEA)
CCS (DS)
CCS (Oxy)
Scores relative to original Ecoinvent values

## Slide 24: Example of transformation: BIOFUELS
(1 MJ biofuel, including combustion)

## Slide 25: Indicators evolution across IAM models for <2 °C scenarios
Impacts of 1 kWh of global electricity, relative to 2020
GHG emissions decrease, but some resource use indicators increase.
Indicators relating to toxicity and ozone depletion are uncertain, but still relevant (e.g., what’ll happen if we do not change our current practices?).

## Slide 26: Climate change impacts across time and scenarios
Substantial impact reductions across sectors
Much is due to lower GHG per kWh of electricity and electrification
Results strongly depend on the scenario and the IAM
Base = No climate mitigiation
RCP 2.6 = <2 °C
RCP 1.9 = 1.5 °C
* Not from IAM scenario

## Slide 27: CASE USING pLCA DATABASE: Electric vehicles and Metals
copper
zinc
nickel
ferronickel
lead
Harpprecht 2021
Based on Mendoza 2018
Climate change results for metals, including electricity change, ore degradation, technology mix, and recycling
-70%
Climate change results for a large size battery electric car operated in Europe, using a «static», reference and <2 C REMIND energy scenarios.
-30%
-42%
Notes: Similar picture for the building sector, metals, chemical products…

## Slide 28: CASE USING pLCA DATABASE: ammonia production (Boyce et al., 2024)
IEA ammonia scenarios + premise
GHG emissions from global ammonia production can be substantially lowered
Key factors:
  future demand
  supply of clean electricity
  shift to green hydrogen
  CCS
Key limitation:
Need for urea delays H2-based options
3-4°C
2°C
1.5°C

## Slide 29: CASE USING pLCA DATABASE: cement production (Müller et al., 2024)
Based on IMAGE scenarios + premise
GHG emissions from global cement production may be substantially lower in the future
CCS is a major factor in this (next to electricity) and so there is considerable uncertainty to these results
There may also be trade-offs with other environmental impact categories

## Slide 30: CASE USING pLCA DATABASE: HYDROGEN (WEI et al., 2024)
Based on IEA H2 scenarios + premise
Fossil fuel-based technologies have limited potential without CCS
Global H2 production grow four to eight times by 2050 but GHG emissions may already peak between 2025 and 2035.
Cumulative GHG emissions may correspond to almost 12% of the remaining carbon budget to meet the 1.5°C target.
Investments in natural gas steam methane reforming with carbon capture and storage, as projected by the IEA, lead to the risk of carbon lock-in.
GHG emissions of one kg H2 of regional markets in 2020 and 2050. a shows GHG emissions of per kg H2 from 15 regional H2 market, as well as market share of different H2 technologies in China, USA and EU in 2020

## Slide 31: Challenges for generating and using pLCA databases
Challenge | Description
Temporal consistency FG/BG | Ensure that the TRL and deployment foreground technology is consistent with the background scenario.
Narrative consistency FG/BG | 
Sectoral coverage | What are the most important sectors’ projections to integrate in LCA?
Environmental coverage | IAM and energy model projections focus on energy and climate. Non-climate impacts are less robust and consistent (e.g., biodiversity, ozone depletion).
Consistency vs. Quality/Detail | Should LCA process be 100% consistent with the scenario (efficiency, lifetime) or should we focus on completeness?
Harmonization & acceptance | Which scenarios should be considered? IPCC’s marker scenarios?
Sharing/distribution | Licensed IAM and LCA data hamper distribution.
Software | Only Brightway and Activity-Browser handle scenario-based LCA databases.
Interpretation | Exploratory scenarios, not predictions!

## Slide 32: Vision: “Qualities” of pLCI databases
Goal:
Meaningful decision support from prospective LCA
Documentation & Guidance
Institutions
pLCI databases
Software providers
Useful
Accessible
LCA software
Usable
Interpretable
Well-maintained
Generation
Sharing
Use
LCI data providers
Integration software
Science-based
LCA
practitioners
Scenario integrators
LCI database
Scenario data
Scenario generators
Broad sectoral and environmental coverage
Easy to work with in LCA software
Practitioners understand the scenarios
Regular updates and improvements
Best available data & models, transparent, reproducible, consistent
Practitioners can easily obtain them
A collaborative effort of all stakeholders is required to make this happen
Steubing, B., Mendoza Beltran, A. & Sacchi, R. Conditions for the broad application of prospective life cycle inventory databases. (2023)

## Slide 33: How DO I obtain premise databases?
Premise databases rely on the underlying ecoinvent database: license restrictions! Two options:
1) I create my own databases
  Install and get familiar with Python
  Install premise
  Run premise, generate databases and export in the desired format
2) I import databases via Activity Browser:
  ScenarioLink plugin (you need a locally installed version of the ecoinvent database)
ScenarioLink Plugin, Activity Browser
33

## Slide 34: FUTURE DEVELOPMENTS
Heat integration
Currently, only mobile heat generators decarbonize
Metals tracking
Mining inventories for ~80 specialty metals
MFA  recycling rates, ore degradation
Scenarios from three additional IAMs
Message-ix, Ti-IAM, GCAM
pathways
A new library for scenario- or sector-wide pLCA

## Slide 35: PATHWAYS: System-wide prospective LCA
Scenario
Mapping
Meta data
2000
A
2100
1
2
4
3
5
Data package
6
B
A
B
Data coupling
Processing
Scenario
database
Additional inventories
Premise outputs data packages containing scenario-adjusted inventories for each time step
Pathways reads data packages and returns impacts by scenario variable (final energy consumer), life-cycle activity, the origin of impacts, and year.

## Slide 36: PATHWAYS: Swiss Final Energy supply
1
2
36

## Slide 37: Conclusions
Good scenarios matter! For LCA results, for stakeholder opinions, and for decision-making. Important to get this right!
The systematic generation of pLCA databases is an exciting and important development for prospective LCA.
pLCA databases are increasingly being used (at least in academia).
Much work remains to improve these databases and prepare them for wider use in LCA practice – collaborative effort is needed!
LIFE CYCLE ASSESSMENT
IMPACT ASSESSMENT
ENERGY SOURCES
CIRCULARITY
SUPPLY CHAINS

## Slide 38: Links to open-source tools
Brightway2 (LCA framework): https://github.com/brightway-lca
Activity-Browser (GUI for Brightway): https://github.com/LCA-ActivityBrowser/activity-browser
Brightway-superstructure (superstructure approach): https://github.com/LCA-ActivityBrowser/brightway-superstructure
wurst (systematic transformation of LCA databases): https://github.com/polca/wurst
premise (IAM-LCA coupling): https://github.com/polca/premise
Pathways (system-wide pLCA): https://github.com/polca/pathways

## Slide 39: Selected references
Methodology
Sacchi R, Terlouw T, Siala K, Dirnaichner A, Bauer C, Cox B, Mutel C, Daioglou V, Luderer G (2022) PRospective EnvironMental Impact asSEment (premise): A streamlined approach to producing databases for prospective life cycle assessment using integrated assessment models Renewable Sustainable Energy Rev 160:112311 doi:https://doi.org/10.1016/j.rser.2022.112311
Mendoza Beltran A, Cox B, Mutel C, van Vuuren DP, Font Vivanco D, Deetman S, Edelenbosch OY, Guinée J, Tukker A (2018) When the Background Matters: Using Scenarios from Integrated Assessment Models in Prospective Life Cycle Assessment J Ind Ecol doi:10.1111/jiec.12825
Steubing B, de Koning D (2021) Making the use of scenarios in LCA easier: the superstructure approach Int J Life Cycle Assess 26:2248-2262 doi:10.1007/s11367-021-01974-2
Use of broad future scenarios (list not comprehensive)
Cox B, Mutel CL, Bauer C, Mendoza Beltran A, van Vuuren DP (2018) Uncertain Environmental Footprint of Current and Future Battery Electric Vehicles Environ Sci Technol 52:4989-4995 doi:10.1021/acs.est.8b00261
Cox B, Bauer C, Mendoza Beltran A, van Vuuren DP, Mutel CL (2020) Life cycle environmental and cost comparison of current and future passenger cars under different energy scenarios Applied Energy 269:115021 doi:https://doi.org/10.1016/j.apenergy.2020.115021
Harpprecht C, Oers L, Northey SA, Yang Y, Steubing B (2021) Environmental impacts of key metals' supply and low‐carbon technologies are likely to decrease in the future J Ind Ecol 25:1543-1559 doi:10.1111/jiec.13181
van der Meide M, Harpprecht C, Northey S, Yang Y, Steubing B (2022) Effects of the energy transition on environmental impacts of cobalt supply: A prospective life cycle assessment study on future supply of cobalt J Ind Ecol n/a doi:https://doi.org/10.1111/jiec.13258
Li C, Mogollón JM, Tukker A, Dong J, von Terzi D, Zhang C, Steubing B (2022) Future material requirements for global sustainable offshore wind energy development Renewable Sustainable Energy Rev 164:112603 doi:https://doi.org/10.1016/j.rser.2022.112603
Xu C, Steubing B, Hu M, Harpprecht C, van der Meide M, Tukker A (2022) Future greenhouse gas emissions of automotive lithium-ion battery cell production Resources, Conservation and Recycling 187:106606 doi:https://doi.org/10.1016/j.resconrec.2022.106606
Zhong X, Hu M, Deetman S, Steubing B, Lin HX, Hernandez GA, Harpprecht C, Zhang C, Tukker A, Behrens P (2021) Global greenhouse gas emissions from residential and commercial building materials and mitigation strategies to 2060 Nature Communications 12:6126 doi:10.1038/s41467-021-26212-z
Yang X, Hu M, Tukker A, Zhang C, Huo T, Steubing B (2022) A bottom-up dynamic building stock model for residential energy transition: A case study for the Netherlands Applied Energy 306:118060 doi:https://doi.org/10.1016/j.apenergy.2021.118060
Dirnaichner, A. et al. Life-cycle impacts from different decarbonization pathways for the European car fleet. Environ. Res. Lett. 17, 044009 (2022).
Sacchi, R., Bauer, C., Cox, B. & Mutel, C. When, where and how can the electrification of passenger cars reduce greenhouse gas emissions? Renew. Sustain. Energy Rev. 162, 112475 (2022).
Sacchi, R., Bauer, C. & Cox, B. L. Does Size Matter? The Influence of Size, Load Factor, Range Autonomy, and Application Type on the Life Cycle Assessment of Current and Future Medium? The Heavy-Duty Vehicles. Environ. Sci. Technol. 55, 5224–5235 (2021).
Ueckerdt, F. et al. Potential and risks of hydrogen-based e-fuels in climate change mitigation. Nat. Clim. Chang. 2021 115 11, 384–393 (2021).
Watanabe, M. D. B., Cherubini, F. & Cavalett, O. Climate change mitigation of drop-in biofuels for deep-sea shipping under a prospective life-cycle assessment. J. Clean. Prod. 364, 132662 (2022).
Gibon, T., Menacho, À. & Guiton, M. Carbon Neutrality in the UNECE Region: Integrated Life-cycle Assessment of Electricity Sources UNITED NATIONS ECONOMIC COMMISSION FOR EUROPE. https://unece.org/sites/default/files/2022-04/LCA_3_FINAL March 2022.pdf (2021).
Cavalett, O., Watanabe, M. D. B., Fleiger, K., Hoenig, V. & Cherubini, F. LCA and negative emission potential of retrofitted cement plants under oxyfuel conditions at high biogenic fuel shares. Sci. Reports 2022 121 12, 1–14 (2022).
Dávila, J., Sacchi, R. & Pizzol, M. Preconditions for CCUS to deliver climate neutrality in cement production. Appl. Energy.
Lamers, P., Ghosh, T., Upasani, S., Sacchi, R. & Daioglou, V. Linking life cycle and integrated assessment modeling to evaluate technologies in an evolving system context: a Power-to-Hydrogen case study for the United States. Environ. Sci. Technol.
Strathoff, P. et al. On the Design and Sustainability of Commuter Aircraft with Electrified Propulsion Systems. AIAA Aviat. 2022 Forum (2022) doi:10.2514/6.2022-3738.

## Slide 40
Learn more about PSI-LEA at https://www.psi.ch/en/lea.
Learn more about ETH-ESA at
https://esa.ethz.ch/.